## Slide 1: Five-Stage Pipeline CPU
Su Qidong

## Slide 2: General Design
Keep it simple and stupid
A ordinary 5-five pipeline
懒得做

## Slide 3: Pipeline
Cache?
  Without cache -> 5 cycles to fetch an instruction
  Fake pipeline
  I-Cache is necessary

## Slide 4: Cache
1 KB I-Cache
D-Cache?
  Timing fail
  Very limited size

## Slide 5: Control
Structural hazard between MEM and IF
Hazard control unit -> MemCtrl
Automata
Avoid useless cycles

## Slide 6: Prediction?
Dynamic ?
  Too complicated
Static ?
  Always take
    Require to calculate the address before EX
  Always don’t take

## Slide 7: Boost!
Eg. Pi
100MHz -> 150MHz
2.4s -> 1.6s
In fact, I didn’t do anything.

## Slide 8: Balance
Design
  Sophisticated
  Simple
High clock rate = Performance?